This lab was dedicated to learn how to use the LM555 Precision Timer, 393 Dual 4-Bit Ripple Counter, and the 138 1-of-8 Decoder in a circuit. The goal of the lab is was to flip through logical 1 and 0 throughout all of the outputs on the Decoder.
Setting up the Timer was tricky because of all of the interconnections of 1 pin to another pin. Interconnections such as: pin 2 joining to the connection from pin 6 to the VCC, pin 6 connecting to pin 7 to the VCC, and pin 8 connecting to both 7 and 6 to the VCC. The Timer required 2 resisters: 1 Brown Black Green, and 1 Brown Black Orange. The output on pin 3 connects to the Counter on the Counter’s pin 1.
The Counter started off with an input from the Timer on pin 1. The main objective for this chip was to bridge the outputs over to the Decoder inputs. The Counter used 3 outputs and therefore the Decoder used 3 inputs. The pins for the outputs for the Counter are: 3, 4, and 5. The pins for the inputs for the Decoder are: 1, 2, and 3.
For the Decoder, the main objective is to have all of the outputs, besides pin 7, working when the Timer dictates the logical 1 or 0. For this lab, we used all the outputs on the 2nd half of the chip (pins 9 – 16). We connected all of our designated outputs to LEDs which used 7 resisters of colors: Brown, Black, and Orange.
The most difficult part of this lab was setting up the Timer due to the complex diagram that was needed. Wire management was also a priority because of how much hardware was required to complete this lab. Deciding whether to use short wires, long wires, placement of LEDs and resistors, was all part of the fun during this lab.